## Slide 1: Image is NOT Perfect Sometimes

## Slide 2: Image Enhancement for Visually Impaired Patients
http://www.eri.harvard.edu/faculty/peli/projects/enhancement.html

## Slide 3
Image Enhancement
Introduction
Spatial domain techniques
    Point operations
    Histogram equalization and matching
    Applications of histogram-based enhancement
Frequency domain techniques
    Unsharp masking
    Homomorphic filtering*

## Slide 4: Recall:
There is no boundary of imagination in the virtual world
In addition to geometric transformation (warping) techniques, we can also photometrically transform images
  Ad-hoc tools: point operations
  Systematic tools: histogram-based methods
  Applications: repair under-exposed or over-exposed photos, increase the contrast of iris images to facilitate recognition, enhance microarray images to facilitate segmentation.

## Slide 5
Point Operations Overview
Point operations are zero-memory operations where
a given gray level x[0,L] is mapped to another
gray level y[0,L] according to a transformation
L
L
x
y
L=255: for grayscale images

## Slide 6: Lazy Man Operation
L
L
x
y
No influence on visual quality at all

## Slide 7
Digital Negative
L
x
0
L

## Slide 8
Contrast Stretching
L
x
0
a
b
ya
yb

## Slide 9
Clipping
L
x
0
a
b

## Slide 10
Range Compression
L
x
0
c=100

## Slide 11: Summary of Point Operation
So far, we have discussed various forms of mapping function f(x) that leads to different enhancement results
  MATLAB function >imadjust
The natural question is: How to select an appropriate f(x) for an arbitrary image?
One systematic solution is based on the histogram information of an image
  Histogram equalization and specification

## Slide 12
Histogram based Enhancement
Histogram of an image represents the relative frequency
of occurrence of various gray levels in the image
MATLAB function >imhist(x)

## Slide 13: Why Histogram?
Histogram information reveals that image is under-exposed
It is a baby in the cradle!

## Slide 14: Another Example
Over-exposed image

## Slide 15: How to Adjust the Image?
Histogram equalization
  Basic idea: find a map f(x) such that the histogram of the modified (equalized) image is flat (uniform).
  Key motivation: cumulative probability function (cdf) of a random variable approximates a uniform distribution
Suppose h(t) is the histogram (pdf)

## Slide 16
Histogram Equalization
Uniform
Quantization
Note:
L
1
x
L
y
0
cumulative probability function
http://en.wikipedia.org/wiki/Inverse_transform_sampling

## Slide 17: MATLAB Implementation
function y=hist_eq(x)
[M,N]=size(x);
for i=1:256
h(i)=sum(sum(x= =i-1));
End
y=x;s=sum(h);
for i=1:256
I=find(x= =i-1);
y(I)=sum(h(1:i))/s*255;
end
Calculate the histogram
of the input image
Perform histogram
equalization

## Slide 18
Image Example
before
after

## Slide 19
Histogram Comparison
before equalization
after equalization

## Slide 20: Adaptive Histogram Equalization
http://en.wikipedia.org/wiki/Adaptive_histogram_equalization

## Slide 21: Histogram Specification/Matching
S
T
S-1*T
histogram1
histogram2
?
Given a target image B, how to modify a given image A such that
the histogram of the modified A can match that of target image B?

## Slide 22: Application (I): Digital Photography

## Slide 23: Application (II): Iris Recognition
before
after

## Slide 24: Application (III): Microarray Techniques
before
after

## Slide 25
Application (IV)

## Slide 26: Application (V): Entertainment
LDR video
Histogram-equalized
Adaptive histogram
-equalized1
1Eric P. Bennett and Leonard McMillan. “Video enhancement using per-pixel virtual exposures,” In ACM SIGGRAPH 2005

## Slide 27
Image Enhancement
Introduction
Spatial domain techniques
    Point operations
    Histogram equalization and matching
    Applications of histogram-based enhancement
Frequency domain techniques
    Unsharp masking
    Homomorphic filtering*

## Slide 28
Frequency-Domain Techniques (I): Unsharp Masking
g(m,n) is a high-pass filtered version of x(m,n)
• Example (Laplacian operator)

## Slide 29: MATLAB Implementation
% Implementation of Unsharp masking
function y=unsharp_masking(x,lambda)
% Laplacian operation
h=[0 -1 0;-1 4 -1;0 -1 0]/4;
dx=filter2(h,x);
y=x+lambda*dx;

## Slide 30
1D Example
x(n)
xlp(n)
g(n)=x(n)-xlp(n)

## Slide 31
2D Example
>roidemo
MATLAB command

## Slide 32: Frequency-Domain Techniques (II): Homomorphic filtering
Illumination
(low freq.)
reflectance
(high freq.)
Basic idea:
freq. domain enhancement

## Slide 33: Image Example
before
after

## Slide 34: Summary of Nonlinear Image Enhancement
Understand how image degradation occurs first
  Play detective: look at histogram distribution, noise statistics, frequency-domain coefficients…
  Model image degradation mathematically and try inverse-engineering
Visual quality is often the simplest way of evaluating the effectiveness, but it will be more desirable to measure the performance at a system level
  Iris recognition: ROC curve of overall system
  Microarray: ground-truth of microarray image segmentation result provided by biologists